## Slide 1
HMI SOFTWARE ARCHITECT — INTERVIEW RESEARCH
Hexagonal
Architecture
Ports & Adapters · Inside-Outside Symmetry · HMI Software
Purpose:
Demonstrate research depth, curiosity, and architectural understanding for the Daimler Truck Driver Experience / Instrument Cluster role.
Primary source: Alistair Cockburn, "Hexagonal Architecture" (2005) — the original paper
Audience: Technical / Software Development | Shareable with any stakeholder
Prepared by Andrew (AJ) Marchese • DevOps Engineer II, DTNA
INFRASTRUCTURE
INFRASTRUCTURE
PORTS
PORTS
DOMAIN
Logic
&
Entities
HMI
Adapter
CAN
Adapter
DB
Adapter
Mock
Adapter
References: Cockburn (2005) · HappyCoders Guide (Woltmann) · github.com/AndrewJesse/HexagonalArchitecture (Golden Path)

## Slide 2
01 Origins — Alistair Cockburn's 2005 Paper (The Primary Source)
The Real Problem: Business Logic Infiltration
Cockburn's original motivation — logic leaks into UI and database layers, making automated testing impossible and batch operation unworkable. Sound familiar for HMI clusters?
The Inside-Outside Asymmetry
The key insight is NOT left vs. right, but INSIDE vs. OUTSIDE. Code inside the hexagon must never leak outside. This single rule replaces all layered-architecture promises that teams historically break.
Why a Hexagon? (Not Because 6 Matters)
"The hexagon is not a hexagon because six is important, but to allow room to insert ports as needed, not being constrained by a one-dimensional layered drawing." — Cockburn, 2005
DDD + Dependency Inversion (SOLID)
HA operationalizes DDD domain isolation. Bob Martin's Dependency Inversion — high-level policy must not depend on low-level detail — is the mechanism that enforces the inside-outside rule.
Maintenance Cost Over Time
Chart: 
| Yr 1 | Yr 2 | Yr 3 | Yr 4 | Yr 5
Tight Coupling | 10 | 24 | 52 | 95 | 160
Hexagonal HA | 14 | 20 | 28 | 36 | 44
" Create your application to work without either a UI or a database so you can run automated regression-tests against the application. "
— Cockburn, 2005 (opening line)

## Slide 3
02 The Hexagonal Model — Domain, Ports & Adapters
DOMAIN
Entities
Use Cases
Business Rules
Event Handlers
PORTS (interfaces — the application boundary)
PORTS (interfaces — the application boundary)
PRIMARY (Driving) ADAPTERS
HMI Event Handler
REST Controller
CLI / Test Driver
CAN Signal Receiver
Drives the use case.
"Primary Actor" in Cockburn's use case model.
SECONDARY (Driven) ADAPTERS
PostgreSQL Repo
CAN Bus / LIN Driver
Message Broker
Mock / In-Memory Stub
Driven by the app.
"Secondary Actor" — answers queries or receives events.
Cockburn's Rule: "Code pertaining to the inside part should not leak into the outside part." Adapters implement port interfaces. Dependency arrow always points inward.
Debug: Failures isolate to adapter boundaries → fast defect pre-analysis
Test: Domain tests with zero hardware — CI runs in milliseconds
Extend: New protocol = one new adapter, zero domain changes

## Slide 4
04 HA in HMI, AUTOSAR & ISO 26262 — Automotive Alignment
AUTOSAR Classic — Layered SW Architecture
Application Layer (SWC)
≡ Domain Logic
RTE — Runtime Environment
≡ Port Boundary
BSW — Basic Software
≡ Driven Adapters
MCAL — Microcontroller Abstraction
≡ HW Adapter
Hardware (ECU / CAN / Sensors)
ISO 26262 / Functional Safety: HA's port boundaries provide natural partitions for ASIL decomposition. Safety-critical domain logic is isolated from non-critical adapter code — a direct architectural enabler for functional safety analysis.
Qt / HMI Rendering & Industry Adoption
Qt / QML Rendering Adapter
Qt's QML layer is a natural driving adapter — it maps user gestures and display events to use case calls without coupling rendering logic to the vehicle domain. Swap QML for Android HMI: one adapter, zero domain changes.
Bosch / Continental
Ports & Adapters in ADAS middleware separates sensor fusion domain from ECU hardware drivers across variants.
Netflix / Amazon
Swappable DB, cache, and service adapters behind a single domain — identical architecture pattern at cloud scale.
Daimler Truck / DTNA
AUTOSAR SWC/RTE in ECU firmware is structurally identical to HA's domain/port separation — not a coincidence.
HMI Fit: Display rendering, driver input events, and vehicle CAN data are naturally separate bounded contexts. HA's port boundaries formalize what AUTOSAR already does implicitly.

## Slide 5
05 Decomposing & Refactoring: The Strangler Fig Pattern
Named after the Strangler Fig tree — new growth wraps the old trunk until the original is replaced. Zero big-bang rewrites. The only responsible approach for production HMI ECUs.
1
Identify
Seam
Find a natural boundary in the legacy ECU codebase — a CAN signal handler, a display update call, or an API that can be wrapped without disrupting adjacent logic.
2
Introduce
Port
Define an interface (port) the legacy caller now targets. Both old and new implementations satisfy it — the caller is completely untouched and unaware of the change.
3
Build New
Adapter
Implement the port using HA-compliant code. Domain stays pure. The new adapter handles protocol translation, data mapping, error propagation, and ISO 26262 boundaries.
4
Route &
Verify
Gradually route live traffic to the new adapter via feature flags or a proxy layer. Rollback is instant — both adapters co-exist behind the shared port interface.
5
Remove
Legacy
Once validated in production builds, delete the original. The Strangler Fig cycle is complete. Architecture debt is paid without a single high-risk cutover event.
Why it matters for DTNA: Instrument cluster software cannot be rewritten mid-program. Strangler Fig enables safe, incremental HA adoption on safety-critical, ISO 26262-governed, schedule-constrained systems.

## Slide 6
06 Enforcing HA Rules & Training Global Teams
Global Team Context: US (Portland/Detroit) · Germany (Stuttgart) · India (DTICI, Bangalore/Pune)
Architecture Decision Records (ADRs)
Every architectural decision stored as Markdown in /docs/adr/ and reviewed in PRs like code. Gives US, Germany, and DTICI India a shared, auditable, immutable record that survives personnel rotation.
Golden Path Repository
Curated reference repo (domain/, ports/, adapters/, tests/) with CAN stub, Qt mock, import-lint, and CI. DTICI developers clone it before writing production ECU code — eliminates tribal knowledge across time zones. github.com/AndrewJesse/HexagonalArchitecture
Dependency Rule Enforcement via Static Analysis
Assert in CI that domain packages never import from adapter packages — violations fail the PR. Tools: SonarQube (C/C++ + custom rules, enterprise standard), ArchUnit (Java), import-linter (Python), Dependency Cruiser (TS/JS), or custom MISRA lint for embedded.
Coaching DTICI — Architecture as a Teaching Framework
Draw the boundary, place the feature, ask “which zone?” Async office hours US → Germany → DTICI India, with the Golden Path repo as shared ground truth. Regular PR mentoring anchors the pattern without synchronous dependency.

## Slide 7
Why This
Matters
for the Role
Defect pre-analysis → adapter isolation pinpoints root cause without full ECU stack
AUTOSAR alignment → AUTOSAR SWC/RTE is Hexagonal Architecture for automotive ECUs
ISO 26262 → port boundaries enable ASIL decomposition and safety-critical partitioning
Qt/QML → rendering adapter pattern separates display logic from vehicle domain cleanly
DTICI India teams → ADRs + Golden Path repo bridge time zones without synchronous dependency
Documentation culture → every architectural decision is auditable, version-controlled, reviewable
Source: Alistair Cockburn, "Hexagonal Architecture" (2005) • Prepared by Andrew (AJ) Marchese, DTNA
Architecture at a Glance
DOMAIN
Use Cases · Entities
Business Rules
PORTS
PORTS
DRIVING
HMI Event
CAN Signal
CLI / Test
DRIVEN
CAN Bus/LIN
Qt / QML
PostgreSQL
✓ Origins (Cockburn)
✓ AUTOSAR
✓ Core Diagram
✓ Strangler Fig
✓ Debug/Test/Extend
✓ ADRs & DTICI